## Slide 1: Tritiated Methane as an Internal Calibration Source in Dark Matter Detectors
Richard Knoche
Candidacy Talk, May 16th 2013

## Slide 2: Overview
Introduction to Dark Matter
Direct Detection of WIMPs
The Large Underground Xenon Detector (LUX)
Internal Calibration Source
  Gas Phase Experiments
  Liquid Phase Experiments
  Simulations for LUX

## Slide 3: Evidence of Dark Matter
Rotational velocities of
galaxies inconsistent with
Newtonian gravity
Gravitational lensing of
cosmological objects, such as the Bullet Cluster

## Slide 4: Composition of the Universe
Define a density parameter as
  Critical density derived from Friedmann’s Equation
MACHO searches utilizing micro-lensing show < 25% of DM can be due to baryonic DM, Hubble observations show DM halos white dwarfs
    Most DM is nonbaryonic matter

## Slide 5: -CDM Model
Analysis of velocity flows and x-ray emission temperatures, constrain total matter component to
  0.2-0.3
Big Bang Nucleosynethesis models constrain baryonic matter of universe to
0.046
Combining restraints results in “-CDM Model”
4.6 0.1%
22 2 %
7 4 %

## Slide 6: Dark Matter Candidates
Axions and Axinos
Gravitons and Gravitinos
Neutrinos
WIMPs

## Slide 7: Neutrinos
Electrically neutral, weakly interacting particle with low mass
“Hot” Dark Matter
Three flavor states, composed of superposition of three mass states
m2 = (7.66 0.35) x 10-5 eV2 for solar neutrino doublet
m2 = (2.38 0.27) x 10-3 eV2 Remaining mass difference

## Slide 8: Neutrinos
Density parameter for neutrinos is given by
Using lower mass limit of neutrinos from hierarchy this gives
0.00122
Galaxy clustering measurements, CMB observations, and Lyman- observations give an upper limit for all hot dark matter of
0.0155
Neutrinos provide some contribution to 22 2 %, but aren’t the primary component

## Slide 9: Cold Dark Matter
Maxwell-Boltzmann statistics say number of particles with m > T will diminish exponentially (in thermal equilibrium)
Use this to derive a density parameter for CDM
2
For Total equal to unity must be on the same order as particles interacting on the electroweak scale
  “The WIMP Miracle”
WIMPs theorized to have mass range from ~10GeV to a few TeV

## Slide 10: WIMPs and SUSY
SUSY requires supersymmetric partner particles exist for each standard model particle
  Sleptons, squarks, gauginos, higgsinos
  Haven’t been discovered, thought to be very massive
Neutral gauginos and neutral higgsinos are theorized to mix into a superposition called the neutralino
  Lightest supersymmetric particle (LSP)
LSP is stable in models which conserve R-parity
  Possible candidate for dark matter
Predicted cross section of 0.192 <  < 0.263 (Dependent on SUSY parameter space)

## Slide 11: Direct Detection of WIMPs
WIMPs interact via nuclear recoils in terrestrial detectors
Expect energy recoil spectrum given by
Cross section has spin-independent (SI) and spin-dependent (SD) components

## Slide 12: Direct Detection of WIMPs
Lighter target nuclei produce lower event rates due to A2 dependence of cross section
Heavier nuclei have a sharper recoil energy spectrum due to form factor suppression
Other events include:
  Electron recoils
    Gamma rays and X-rays
  Nuclear recoils
    WIMPs and neutrons

## Slide 13: The LUX Detector
Dual phase time projection chamber
350 kg of xenon
PMT arrays in liquid and gas
Scintillation (S1) and
ionization (S2) signals

## Slide 14: Calibration of the Detector
  Nuclear recoils have higher ionization density,
    leads to higher recombination probability, and higher S1/S2 ratio
  Neutron source is used to generate nuclear recoil band
Beta or gamma emitter is used to generate electron recoil band
  Typically external Cs-137 source
Xenon in LUX is self-shielding
  Scattering Length ~ 30 cm at
  174 nm wavelength
  External sources do not
  penetrate far enough

## Slide 15: Internal Calibration Source
Single beta emitter in energy range of interest (<15 keV)
Low electronegativity so that drift length is unaffected
Can not attenuate UV scintillation
Can dissolve into liquid xenon
Long enough life time to diffuse throughout detector
Must be removable after use
  Short enough life time to decay away
  Alternatively, something that can be removed through purification

## Slide 16: Tritium as an Internal Source
Beta emitter with Q-value of 18.6 keV
Broad spectrum over entire energy range of interest
12.3 year half life
  Will diffuse through detector
  Must be purified away
Sticks to most surfaces
  Teflon, polyethylene, steel, etc.

## Slide 17: Tritiated Methane
Methane is inert due to fully saturated carbon-hydrogen bonds.
Diffusion constant in polyethylene that is 10 times smaller than hydrogen
Low electronegativity
Use tritated methane (CH3T) as an internal calibration source!

## Slide 18: Gas Phase Experiment – Goals and Setup
Determine purification efficiency and study residual contamination in system.

## Slide 19: Gas Phase Experiment – Results
Histogram of Purification Efficiency
Define purification efficiency
Achieved purification efficiencies ranging from 99.2%-99.997%

## Slide 20: Gas Phase Experiment – Results
High flow rate lead to lower purification efficiency
  Worst purification efficiency (96% corresponds to highest flow rate (8 SLPM). Typical flow rate was 0.3 SLPM.

## Slide 21: Gas Phase Experiment – Results
Increasing time between purifications increases purification efficiency.

## Slide 22: Gas Phase Experiment – Results
Tritated methane must be swept out of injection space
Tritiated methane must be purified prior to injection

## Slide 23: Liquid Phase Experiment – Goals and Setup
Apply what we learned in gas phase experiment to obtain high purification efficiency in liquid phase

## Slide 24: Liquid Phase Experiment- Results
Purification Efficiency Ranged from 0.999832 to 1.000087
  Average of 99.9989% purification
  Plastics made no difference in purification efficiency

## Slide 25: Liquid Phase Experiment- Results

## Slide 26: Liquid Phase Experiment- Results
Injected over 68,000 Bq with no rise in residual background rate
  Linear fit has slope of 4.3e-7
  Jump in rate in polyethylene data is from gain change

## Slide 27: Liquid Phase Experiment- Out Gassing Study
First examined purification efficiency with polyethylene in the system
  Take background data, inject, purify away

## Slide 28: Liquid Phase Experiment- Results
Bypass the purifier to study outgassing rate
  See two features – steps and gradual rise

## Slide 29: Liquid Phase Experiment- Results
Closer look at the steps – are they really tritium?
  8833 events -> 13156 114.70 events -> 17190 131.11 events

## Slide 30: Liquid Phase Experiment- Results
Two possible explanations
  Gain is drifting (shifts spectrum horizontally)
  More tritium is showing up (shifts spectrum vertically)
Use cesium-137 peak to search for changes in gain
  No change in gain Must be from pockets of tritium

## Slide 31: Conditions for a Successful Calibration
Need enough calibration events to accurately measure tritium spectrum
  Define “enough calibration events” as a factor of 100 over number of background events in 300 days
  Sets a goal of about 17,000 events from calibration
Calibration can not significantly add to the background rate after being purified
  Define tolerable contribution to the background rate as 5% increase
  Sets limit on residual activity from calibration at 0.33 Bq

## Slide 32: Determining How Much Activity to Inject into LUX
Fick’s first and second laws describe diffusion process
Diffusion constant of methane in polyethylene at room temperature is
  Temperature dependence modeled by Arrhenius equation
  Suggests a factor of 10-6 adjustment to diffusion constant at liquid xenon temperatures
    Equivalent to increasing the thickness of plastic by factor of 1,000
    Motivates use of half-infinite boundary conditions in diffusion model

## Slide 33: Determining How Much Activity to Inject into LUX
Analytic solution to Fick’s second law using half-infinite boundary conditions
Plug into Fick’s first law, evaluate at x=0 for out gassing
Define new constant

## Slide 34: Determining How Much Activity to Inject into LUX
Fit to outgassing
data to determine G
  0.001 < G < 0.01

## Slide 35: Determining How Much Activity to Inject into LUX
Use constraints on G to numerically model CH3T rate in LUX after a calibration
  Use Fick’s laws to get flux from out gassing (J)
  Use time dependent concentration that includes out gassing and purification

## Slide 36: Determining How Much Activity to Inject into LUX
0.1 Bq injection gives ~15,000 events and reaches 5% of background in one to two months for all G values

## Slide 37: Tritium Injection System for LUX
Range on injection activities from 0.00625 Bq to 0.4 Bq
No cryopumping required
Flow Through Expansion Volumes
35 Bq Tritiated Methane Source

## Slide 38: Conclusion
Dark Matter is thought to consist of WIMPs
  LUX is searching for nuclear recoils from WIMPs
It is possible to use tritiated methane as an internal calibration source in xenon detectors
  Hot zirconium getter can remove >99.98% of injected activity
  Care must be taken to model outgassing and purification effects on injection activity
To meet LUX’s goal of ~17,000 calibration events with a return to 5% of initial background a 0.1 Bq injection is required